Moore’s Law states that the density of transistors will double every two years.

Some of the factors that prevent Moore’s Law from being satisfies are that:

- Increasing the density of transistors means adding more transistors, therefore they consume more power.
- The increased power output reflects as increased temperature which can burn the processor if too much.
- Dynamic power consumption cannot allow the frequency to increase so much according to the formula:
  P = a * CF(V)^2
- Voltage Scaling (V) must remain large enough to be within the transistor threshold voltage.
- Voltage scaling cannot prevent leakage power loss due to the transitor density being smaller, therefore insulators between conductors will become smaller.